## Slide 1: Robot Learning Control: Gaussian Process Robotics II 2019-2020
Fioretti Gianmarco Mauro Alessandro Nicotra Emanuele
Special Thanks to Marco Capotondi

## Slide 2: Introduction
Robot Learning Algorithm
Goal: Make a robot system execute tasks as regulation and trajectory tracking in a very accurate way.
Standard control methods:
FFW+PD: Inversion of the dynamics model in order to calculate the necessary torque that minimizes the error between the robot reference configuration and the actual one.
Computed Torque: A control method which corresponds to use the dynamic model over the system considering the joint decoupled. More precise, energy-efficient and suitable for complaint robots (

## Slide 3: Introduction
Robot Learning Algorithm
Problems:
Exact knowledge of the dynamic robot model is required.
Mismatches between the nominal dynamic model and the actual behaviour of the robot appear.
Lack of optimality and robustness
Solutions:
Robot learning algorithms are the suitable tools to better approximate the dynamic model and being able apply a correction to the Feedback Linearization and so correctly linearize the system.
Choice of the algorithm:
Gaussian Process Regression is the method we are going to explain and implement in the following. It will be implemented over the corresponding torque errors, between the nominal dynamic model and the ”real one”.

## Slide 4: Robot Models
2R Planar Robot
Nominal Robot Model
 | Link 1 | Link 2
a | 2 | 1
θ | q1 | q2
d | 0 | 0
α | 0 | 0
m | 1 | 1

## Slide 5: Robot Models
2R Planar Robot
Real Robot Model
 | Link 1 | Link 2
a | 2.1 | 0.8
θ | q1 | q2
d | 0 | 0
α | 0 | 0
m | 1 | 1.16

## Slide 6: Computed Torque
Simulation
 | Joint 1 | Joint 2
 | Joint 1 | Joint 2

## Slide 7: Computed Torque
Simulation

## Slide 8: Gaussian Process
– Random Variable
– Probability density function (pdf)
Gaussian distribution
Conditioning
Conditional probability of given
Marginalization
Basics in Probability

## Slide 9: Gaussian Process
Gaussian distributions are closed under conditioning and marginalization
),
),
The resulting distributions and are also Gaussian
Key idea: we want to condition the output y of the
process, given a certain input x, with respect to the data set (X,Y)
Properties of Gaussian Probability Density Funciton

## Slide 10: Gaussian Process
We want to obtain the mean and the covariance of the conditional probability
The covariance is build using the kernel function of the Gaussian Process
This function is evaluated for each pairwise combination of the
given points.
The mean is set equal to zero, even if it
was different from zero we can add it to the resulting function values after the prediction step to translate it.
Mean and Covariance computation

## Slide 11: Gaussian Process
Notation
– Training points set
Input
Output
Test points set
Test point
Function value at the point
White Gaussian noise
covariance matrix between A and B built using the kernel function

## Slide 12: Gaussian Process
Probability density computation (Noise-free)
The joint distribution between the training and the test set is a Gaussian distribution
From which we can obtain the conditional distribution using the conditioning operation, in particular its mean and covariance are respectively
Where
∈

## Slide 13: Gaussian Process
Probability density computation (with noise)
The joint distribution between the training and the test set is a Gaussian distribution
From which we can obtain the conditional distribution using the conditioning operation, in particular its mean and covariance are respectively
Where
∈

## Slide 14: GP Sparsification
Why do we need sparsification?

## Slide 15: GP Sparsification
Such that
Nystrøm Approximation
Instead of

## Slide 16: GP Sparsification
with
Projected Process Approximation
(
)

## Slide 17: GP Sparsification
Projected Process Approximation
With

## Slide 18: GP Sparsification
Heuristic
General for greedy subset selection. is the criterion function evaluated on data point j.
Reference: C. E. Rasmussen & C. K. I. Williams, ”Gaussian Processes for Machine Learning”, the MIT Press, 2006.

## Slide 19: GP Sparsification
With
Heuristic
Reference: J. Schreiter, D. Nguyen-Tuong, M. Toussaint, “Efficient sparsification for Gaussian process regression”, 2016.

## Slide 20: Gaussian Process Regression
Implementation
Data Generation
GP Training
Radial Basis Function Kernel (RBF)
Diagonal weight matrix

## Slide 21: Gaussian Process Regression
Implementation
Hyperparameters Optimization
Max LML (Logarithmic Marginal Likelihood)
Given that

## Slide 22: Offline Gaussian Process
Simulation – Known Trajectory
 | Joint 1 | Joint 2
 | Joint 1 | Joint 2

## Slide 23: Offline Gaussian Process
Simulation – Known Trajectory
Active Point
Active Point

## Slide 24: Offline Gaussian Process
Simulation – Known Trajectory
Active Point
Active Point

## Slide 25: Offline Gaussian Process
Simulation – Unknown Trajectory
 | Joint 1 | Joint 2
 | Joint 1 | Joint 2

## Slide 26: Offline Gaussian Process
Simulation – Unknown Trajectory
Active Point
Active Point

## Slide 27: Offline Gaussian Process
Simulation – Unknown Trajectory
Active Point
Active Point

## Slide 28: Offline Gaussian Process
Simulation – Without Heuristic
Active Point
Active Point

## Slide 29: Online Gaussian Process
Simulation
 | Joint 1 | Joint 2
 | Joint 1 | Joint 2

## Slide 30: Online Gaussian Process
Simulation
Active Point
Active Point

## Slide 31: Online Gaussian Process
Simulation
Active Point
Active Point

## Slide 32: Conclusions
So far, we have achieved the anticipated results
Model mismatches compensation
Lower gains needed
However, there are still some drawbacks as the Generalization error problem.
A very powerful Tool
Thanks for the attention!